## Slide 1
WSN Lab Final Presentation Group 2
Chi Xia
chi.xia@tum.de
Zhihao Deng
zhihao.deng@tum.de
Kaikang Huang
go49jan@mytum.de
Intelligent Parking Lot

## Slide 2
Smart Parking System: Motivation and Objectives
Motivation
Inefficient underground parking leads to time waste and congestion
A wireless sensor network detects space availability in real-time
The system adapts to topology changes and saves power automatically
Drivers receive parking information before turning in
three slots available
Only two nodes work properly
Topology change
Project Objectives
Build a multi-hop smart parking network using at least 7 sensor nodes
GUI for drivers to check available spaces
GUI for developers to monitor topology and node status (failures, updates)
Integrate multiple sensor types for reliable detection and fault tolerance
Provide a user-friendly GUI for drivers to view open spots
Normal Operation
Node Failure Scenario

## Slide 3
Hardware and Software
Hardware
Light Sensor Detects ambient light drop caused by vehicle presence (e.g. shadow under car)
Distance Sensor Measures how close an object (car bumper) is above the spot
nRF52840 boards
  6 boards with sensors (each installed in one parking spot)
  1 board runs GUI and manages network (gateway)
Software
Contiki-NG (written in C)
  Runs on each node
  Collects and processes sensor data
  Performs wireless communication using multi-hop
QT GUI / Python (host-side)
  Visual interface for developers
  Displays available parking spots in real time
  Displays possible topology changes

## Slide 4
MAC protocol and Routing protocol
Routing protocol, TEEN [1]
Clustering hierarchy
Reactive network
Threshold of data determines transmission
Depends on battery to choose head
Head sends heartbeat info
[1] A. Manjeshwar and D. P. Agrawal, "TEEN: a routing protocol for enhanced efficiency in wireless sensor networks," Proceedings 15th International Parallel and Distributed Processing Symposium. IPDPS 2001, San Francisco, CA, USA, 2001, pp. 2009-2015, doi: 10.1109/IPDPS.2001.925197. keywords: {Routing protocols; Intelligent networks; Wireless sensor networks; Temperature sensors; Sensor phenomena and characterization; Energy efficiency; Condition monitoring; Fault tolerance; Costs; Mobile computing},
Inside a Cluster
Node directly connects to head
OR
Apply some algorithm to save energy
Join a node
Broadcast and get feedback
Decide Cluster
Carrier-Sense Multiple Access (CSMA)
Not a time-sensitive application
ACK

## Slide 5
Questions and Suggestions

## Slide 6
Thanks for Listening