## Slide 1: Intelligent Parking Lot WSN Lab Final Group 2
Zhihao Deng, Chi Xia, Kaikang Huang
Chair of Communication Networks
School of Computation, Information and Technology
Technical University of Munich
Munich, July 15 2025

## Slide 2
Project overview
Motivation
Inefficient underground parking leads to time waste and congestion
A wireless sensor network detects space availability in real-time
The system adapts to topology changes and saves power automatically
Drivers receive parking information before turning in
Project Objectives
Build a multi-hop network using 7 sensor nodes
GUI for drivers to check available spaces
GUI for developers to monitor topology and node status (failures, updates)
Integrate two sensor types for reliable detection and fault tolerance

## Slide 4
Hardware and Software
Hardware
Light Sensor Detects ambient light drop caused by vehicle presence (e.g. shadow under car)
Distance Sensor Measures how close car front is to the wall
nRF52840 boards
  7 boards with sensors (each installed in one parking spot)
  1 board runs GUI and manages network (gateway)
Software
Contiki-NG
  Runs on each node
  Collects and processes sensor data
  Performs wireless communication using multi-hop
QT GUI
  Visual interface for drivers and developers
  Displays available parking spots in real time

## Slide 5: Network description and routing technique
Custom RIP-based multi-hop protocol with self-organizing topology
Cluster heads selected based on hop count, RSSI, and battery level
Topology discovery via DIO/DAO exchange; routing tables updated dynamically
Master node maintains global view and broadcasts cluster assignments
Hierarchical data forwarding through cluster heads
Dynamic node joining supported via DIO broadcast and topology re-initiation

## Slide 6: Graphical user interface (GUI)
Left panel of the GUI:
  Open/close serial port, set transmit power
  Show parsed messages from master
  Display light, distance, battery per node
  Indicate parking slot status
  Indicate node status

## Slide 7: Graphical user interface (GUI)
Right panel of the GUI:
  Visualizes real-time network topology and routing updates
  Node types are color-coded:
    🔴 Red: Offline
    🟠 Orange: Normal node
    🔵 Light blue: Cluster head
    🔷 Dark blue: Master node

## Slide 8: Network in different condition
All nodes working -> network constructed
Only one node is working -> selected as cluster head

## Slide 9: Application-specific features
  Customized cluster-based routing with head selection logic
  Routing decisions consider hop count, RSSI, and battery level
  GUI filters short-term value fluctuations to improve display stability and avoid wrong detection
  Sensor data transmission triggered only on significant changes

## Slide 10: Demonstration cases

## Slide 11: Case 1: Initialization and network establishment
Turn on all 7 boards -> topology establishment
Sensor value readout and display
Evaluation of parking slot status (green -> parking slot available,
red -> parking slot possessed)

## Slide 12: Case 2: Dynamic routing
New node discovery:
1. turn on a new board (e.g. node 6)
2. Node listens to channel 12 for 5 times
3. if no flooding message is received
4. send discovery signal to neighbor nodes
5. master initialize network reset

## Slide 13: Case 2: Dynamic routing
Existing node failure:
  turn off a working node (simulate node failure)
  master does not receive its heartbeat signal
  master initialize network reset

## Slide 14: Case 3: Reactive network
Sensor value will only be transmitted and displayed when it changes dramatically (change of light > 50 lux or distance > 10cm)

## Slide 15: Case 4: Low-energy awareness routing

## Slide 16
Thanks for Listening
Any questions or feedback?